## Slide 1: Vision, Brain and Assistive Technologies
Zhigang Zhu, Herbert G. Kayser Chair Professor
Department of Computer Science
CUNY City College and Graduate Center
Vision and Brain
How We Perceive the World
1. Eyes

## Slide 2: Acknowledgments
Textbook:
  Vision and Brain - How We Perceive the World, By James V. Stone, The MIT Press
Slides:
  Most of the figures were taken from the textbook (with permission for use in this class). Please do not distribute or use them for other purposes

## Slide 3: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 4: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 5: Vision: An Overview
How We See: The Brain as a Detective
Illusions: How the Brain Fails?
Recognizing Objects
Perceiving 3D Shape
Color and Shade
Brain and Vision

## Slide 6: How We See: The Brain as a Detective
The brain is constantly doing its best to find out what in the world is responsible for the image on the retina. In essence, this is the central problem of vision.
It’s as if the brain is a detective at the scene of a murder, with the retinal image as forensic evidence on the body. But this is a case that would defeat even the great Sherlock Holmes.

## Slide 7: Illusions: How the Brain Fails?
Disappearing lines of the
World Wildlife Fund panda logo between 1961 and 2006.
Kanizsa triangles show that some lines are more apparent than real.

## Slide 8: Color Woes
Squares with dots in them are the same color

## Slide 9: Recognizing Objects
Look at the star in the center of the figure. At one moment, the rings appear to be viewed from above, but at the next moment they seem to viewed from below.

## Slide 10: Recognizing Objects
Piano or pile of wood? It all depends on your point of view. By Shigeo Fukuda.

## Slide 11: Perceiving 3D Shape
Are these pictures of a hill or a crater? It all depends on your point of view. Barringer Meteor Crater, reproduced with permission from the United States Geological Survey.

## Slide 12: Color and Shade
Surfaces in shadow are perceived as being lighter.
The second card from the left seems to be a stronger shade of pink in the top picture.
- From Wikipedia

## Slide 13: Color and Shade
©1995, Edward H. Adelson. These checkershadow images may be reproduced and distributed freely.

## Slide 14: Brain and Vision
David Marr (1982, p. 27):
“Trying to understand vision by studying only neurons is like trying to understand bird flight by studying only feathers: it just cannot be done.”

## Slide 15: Brain and Vision
1 Computational theory
  What is the nature of the problem to be solved, what is the goal of the computation, why is it appropriate, and what is the logic of the strategy by which it can be carried out?
2 Representation and algorithm
  How can this computational theory be described in a computer? In particular, what is the representation for the input and output, and what is the algorithm (method) for transforming input to output?
3 Hardware implementation
  How can the representation and algorithm be realized (implemented) physically?
Marr’s computational framework

## Slide 16: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 17: Human and Animal Eyes
The Simple Eye
Human Eye Structure
Human Eye Optics

## Slide 18: The Simple Eye
For our purposes, a simple eye is one that can form an image on the back of the eye or retina with or without a lens.
This design is shared by all vertebrates
  e.g., mammals, reptiles, and fish
  squid and octopuses, jumping spiders, and
  an ancient group of species called “ammonites,” which have only one living relative, the Nautilus.

## Slide 19: Human Eye Structure

## Slide 20: The Human Eye Optics

## Slide 21: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 22: The Pinhole Camera
Image Formation
Pinhole Camera Model
Focal Length, FOV
Equivalent Geometry
Perspective Projection
Observing Pinhole Camera Images

## Slide 23: Image Formation
L
i
g
h
t
(
E
n
e
r
g
y
)
S
o
u
r
c
e
S
u
r
f
a
c
e
P
i
n
h
o
l
e
L
e
n
s
I
m
a
g
i
n
g
P
l
a
n
e
W
o
r
l
d
O
p
t
i
c
s
S
e
n
s
o
r
S
i
g
n
a
l
Camera: Spec & Pose
3D Scene
2D Image
Notes: In the geometric point of view, the camera is a device that convert 3D scenes into 2D images. As we usually do in the real life, the locations and orientations of the camera change in order to capture good views of the scenes. In computer vision, in order to recover the 3D structure of the scenes from their 2D images, we need to build the relations between the 2D images and the 3D scenes, through the camera. The parameters of the camera include two parts: the intrinsic parameters that map the 3D points into 2D images, and the extrinsic parameters that represent the position and orientation (POSE) of the camera

## Slide 24: Pinhole Optics versus Thin Lens

## Slide 25: Pinhole Camera Model
Pin-hole is the basis for most graphics and vision
  Derived from physical construction of early cameras
  Mathematics is very straightforward
3D World projected to 2D Image
  Image inverted, size reduced
  Image is a 2D plane: No direct depth information
Perspective projection
  f called the focal length of the lens
  given image size, change f will change FOV and figure sizes
Notes: First, Let’s have a look at the camera model- without consider the pose of the camera.
In the diagram, f is called the focal length of the (pinhole) lens and is the distance from the center of the lens to the image plane measured along the optical axis. The center of the lens (center of projection) is the point in the lens system through which all rays must pass.
From the diagram, it is easy to see that the image projected onto the image plane is inverted. The ray from the cartoon figure's head, for example, is projected to a point near the bottom of the image plane, while the ray from a point on the figure's foot is projected to a point near the top of the image plane.
Various coordinate reference frames can be associated with the pinhole camera system. In most of them, the Z axis coincides with the optical axis (also called the central projection ray). By convention, the image plane is located at Z = -f and the lens is located at Z = 0. Z is also the distance to an object as measured along the optical axis; also by convention, Z is positive coming out of the camera. The X and Y axis lie in the image place - we will establish exactly how later.
It is possible to reverse the position of the image plane and the camera lens so that the projected image is upright....

## Slide 26: Focal Length, FOV
Consider case with object on the optical axis:
Optical axis: the direction of imaging
Image plane: a plane perpendicular to the optical axis
Center of Projection (pinhole), focal point, viewpoint, nodal point
Focal length: distance from focal point to the image plane
FOV : Field of View – viewing angles in horizontal and vertical directions
f
z
viewpoint
Image plane
Notes: Several important terms for perspective projections
Basic properties: Figure sizes and FOV versus focal length
Image resolutions

## Slide 27: Focal Length, FOV
Consider case with object on the optical axis:
f
z
Out of view
Image plane
Optical axis: the direction of imaging
Image plane: a plane perpendicular to the optical axis
Center of Projection (pinhole), focal point, viewpoint, nodal point
Focal length: distance from focal point to the image plane
FOV : Field of View – viewing angles in horizontal and vertical directions
Increasing f will enlarge figures, but decrease FOV
Notes: Simple geometry of the pinhole camera

## Slide 28: Equivalent Geometry
Consider case with object on the optical axis:
f
z
More convenient with upright image:
f
z
Projection plane z = f
Equivalent mathematically
Notes: These geometries are equivalent mathematically. In the second case, the center of projection is still located at 0 along the optical axis. However, the image plane is placed at z=f.
The equivalence of both geometries can be established by recognizing that the two triangles in the upper diagram are similar to the two triangles in the lower diagram. In fact, it is exactly this relationship which will allow us to derive the perspective projection equations.....

## Slide 29: Perspective Projection
Compute the image coordinates of p in terms of the world (camera) coordinates of P.
Origin of camera at center of projection
Z axis along optical axis
Image Plane at Z = f; x // X and y//Y
x
y
Z
P(
X,Y,Z
)
p(x, y)
Z = f
0
Y
X
Notes: Our goal is to compute the image coordinates of the point P located at (X,Y,Z) in the world coordinate system under perspective projection. Equivalently, we want to know where the ray passing through the point P and the center of the camera lens located at the center of projection (0) pierces the image plane. We can do this rather simply by examining the projections of the point P on the (X,Z) and (Y,Z) planes.
Here we are assuming the camera coordinate system coincides with the world.

## Slide 30: Reverse Projection
Given a center of projection and image coordinates of a point, it is not possible to recover the 3D depth of the point from a single image.
In general, at least two images of the same point taken from two different locations are required to recover depth.
Notes: We have seen that, given the coordinates of a point (X,Y,Z) and the focal length of the lens f, the image coordinates (x,y) of the projection of the point on the image plane can be uniquely computed. Now let us ask the reverse question: Given the coordinates (x,y) of a point in the image, can we uniquely compute the world coordinates (X,Y,Z) of the point? In particular, can we recover the depth of the point (Z)?
To see that this is not possible, consider the infinitely extended ray through the center of projection and the point (x,y) on the image plane. Any point P in the world coordinate system which lies along this ray will project to the same image coordinates. Thus, in the absence of any additional information about P, we cannot determine its world coordinates from knowledge of the coordinates of its image projection.
However, it is easy to show that if we know the image coordinates of the point P in two images taken from different world coordinate locations, and if we know the relationship between the two sensor locations, then 3D information about the point can be recovered. This is known as stereo vision; in the human visual system, our two eyes produce slightly different images of the scene and from this we experience a sensation of depth.

## Slide 31: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam : what do you see in this picture?
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: We may see
Objects : river, river bank, cars parking on the bank, buildings, tree in front of the buildings, bridge, sky.
Can figure out relative distances – SO WHAT? Do we see the 3D structure with just one images?
Let’s first have a look at what geometric properties are preserved in the 2D perspective image.

## Slide 32: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: Straightness is preserved
Proof. x= fX/Z, y=fY/Z: a 3D line in space projects to a 2D line in the image

## Slide 33: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: Size is inversely proportional to the depth (distance) Z

## Slide 34: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: In general, the angles and parallelism are not preserved. For example, the right angles of the rectangular building change: Acute angles (smaller than 90) in the nearer end and obtuse angles (greater than 90) in the farther end….

## Slide 35: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  depth
Notes: The projections of parallel lines converge to a point. --- vanishing point
So the shapes usually change
How about planes parallel to the image plane… we may not be able to find such a plane in this image, but…

## Slide 36: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  parallel to image
  depth
Notes: The façade of building in the far end approximately is parallel to the image plane so the shape is preserved

## Slide 37: Pinhole camera image
- We see spatial shapes rather than individual pixels
- Knowledge: top-down vision belongs to human
- Stereo &Motion most successful in 3D CV & application
- You can see it but you don't know how…
Amsterdam: what do you see?
  straight line
  size
  parallelism/angle
  shape
  shape of planes
  parallel to image
  Depth ?
    stereo
    motion
    size
    structure …
Notes: SO why can we see 3D structure from a single image?
We do not see individual pixels, but rather spatial shapes
We use knowledge of the objects (RECTANGULAR building, similar size of the cars), river and bank in a plane – perceptual organization (up-down vision)
Perspective distortion actually tells us some 3D information: Using the projections of parallel lines in the façade of the building, we can estimate the orientation of the building therefore 3D structure
Order of the object, Occlusion,
BUT it is extremely hard for a computer to use high level knowledge . Up-down paradigm seems to be the privilege of human visual perception. The state-of-the-art of the computer vision mainly use bottom-up approach. SO
Stereo
Motion
The idea is to recover 3D of each small local pieces (point, line, patch), and then group and segment the 3D point cloud into meaningful objects so that the computer may recognize the objects in images
Intermediate results for image and video representations, coding and compression, interactive 3D presentation and event detection
image mosaics for entertainment, interface, virtual reality, and monitoring
Layered representation (MPEG4)
3D video
Motion Detection (of human, cars) for surveillance, traffic monitoring,
Human Vision: You can see it but you don't know how you see it.

## Slide 38: Yet other pinhole camera images
Markus Raetz, Metamorphose II, 1991-92, cast iron, 15 1/4 x 12 x 12 inches
Umass Fine Art Center University Gallery, Sep 15 – Oct 26, 2000
Rabbit or Man?
Notes: What do you see? What are their relation?

## Slide 39: Yet other pinhole camera images
Markus Raetz, Metamorphose II, 1991-92, cast iron, 15 1/4 x 12 x 12 inches
Umass Fine Art Center University Gallery, Sep 15 – Oct 26, 2000
2D projections are not the “same” as the real object as we usually see everyday!
Notes: All of them are 2D projections of the same 3D real object!
Vision is a complicated thing!
What you see is not what it is.

## Slide 40: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 41: Human Eye: A Window to Brain
Basic Facts
An Organ of Imperfection?
Not Blinded by the Light
The Retina
What Does the Eye Not Tell the Brain?

## Slide 42: Human Eye: Basic Facts
24 mm in diameter
Most of the focusing power depends on the fixed shape of the cornea.
The lens simply fine-tunes the focus of the image on the retina.

## Slide 43: An Organ of Imperfection?
Chromatic aberration
Backward retina
Black spot

## Slide 44: Chromatic aberration
Chromatic aberration is the blurring of an image caused by the inability of the lens to focus light of all different colors on the retina at the same time.
In the figure below, light from part of a hat contains a mixture of yellow and blue colors. As light passes through the lens, its path is bent, but the amount of bending depends on the color of the light, with red being bent least, blue being bent most, and yellow light being bent somewhere in between.

## Slide 45: Backward retina
The light rays that contribute to the retinal image have to pass through layer of nerve fibers and the blood vessels before reaching the light-sensitive photoreceptors.

## Slide 46: Visual Impairment Simulation

## Slide 47: Black spot
octopus does not have a blind spot
Retina, as seen through an ophthalmoscope. The branching structures are arteries and veins lying close to the surface of the retina, which converge on the blind spot (optic disk). The dark region to the right is the fovea, and the nose is to the left of this image. The centers of the blind spot and fovea are 4.3 mm apart. Courtesy Robin Farr.

## Slide 48: Not Blinded by the Light
The eye operates over an enormous range of lighting conditions, from moonlight to sunlight, a range that can vary by a factor of 1010 (10 billion).
Such a range cannot possibly be accommodated by changing the pupil area by a factor of 17

## Slide 49: The Retina
Fovea
Cones
Rods

## Slide 50: Fovea
The image is brought to a focus 16 millimeters behind the lens onto the retina
Macula is about 5 mm across and contains a yellow pigment that blocks ultraviolet light.
Within the macula, there is a small circular region about 0.5 mm in diameter (1.7 degrees), the fovea (Latin for “pit”), packed with color-sensitive photoreceptors called cones.
Within the fovea, cones are densely packed at about 200,000 per square millimeter

## Slide 51: Cones and Rods
the overall proportions of cones sensitive to red, green, and blue light are 63, 31, and 6 percent, respectively
rods are exquisitely sensitive and operate only in low-light conditions

## Slide 52: Densities of Rods and Cones
Rod and cone densities across the retina of the left eye.

## Slide 53: What Does the Eye Not Tell the Brain?
The retina contains 126 million photoreceptors, each of which measures the amount of light at one point in the retinal image.
However, the optic nerve, which exits via the back of the eye on its way to the brain, contains only one million fibers (connected with ganglion cells)
It looks as if less than 1 percent (1/126) of the information in the retinal image gets sent to the brain.

## Slide 54: Outline (Ch. 1 and Ch. 2)
Vision: An Overview
Human and Animal Eyes
The Pinhole Camera
Human Eye: an Window to Brain

## Slide 55: Reading List and Resources
Textbook:
  Vision and Brain - How We Perceive the World, By James V. Stone, The MIT Press
Reading:
  IEEE Workshop on Multimodal and Alternative Perception for Visually Impaired People (MAP4VIP 2013) (Papers, Slides & Posters)
  Workshop on Environmental Sensing Technologies for Visual Impairment (ESTVI 13) (YouTube Video)
Additional Reading on Assistive Technologies for Visually Impaired (link to the list - internal use only)