## Slide 1: Introduction
Zhigang Zhu, City College of New York zzhu@ccny.cuny.edu
Human and Computer Vision with Advanced Topics
Feature Extraction
Notes: This course is a basic introduction to parts of the field of computer vision. This version of the course covers topics in 'early' or 'low' level vision and parts of 'intermediate' level vision. It assumes no background in computer vision, a minimal background in Artificial Intelligence and only basic concepts in calculus, linear algebra, and probability theory.

## Slide 2: Human and Machine Vision: what features will be useful?
Notes: It depends on the task. Assume that we want to classify these images.

## Slide 3: Bag-of-pixels
We could create a bag-of-pixels vector for an image
characterize colors by clustering RGB values;
count the number of pixels in an image in each RGB bin
But colors do not capture an image in the same way that words capture a document.

## Slide 4: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 5: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 6: Convolution: an introduction
Filtering: replace each pixel by the weighted combination of that pixel and neighbor pixels; weights are determined by a filter
This function is referred to as convolution
A linear filter produces an identical image:
A blurring filter produces a blurred image:
0 | 0 | 0
0 | 1 | 0
0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
Notes: convolution is very useful for signal processing in general. There is a lot of complex mathematical theory available for convolutions.
You can use a simple matrix as an image convolution kernel/filter to process an image or detect certain features.

## Slide 7: Image filters
https://softwarebydefault.com
0 | 0 | 0
0 | 1 | 0
0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1

## Slide 8: Detecting features: edge
We can use specific filters to identify features in an image
Consider: edges, corners, blobs, patterns (e.g., polka-dots, stripes)
Line detection with 4 filters
https://aishack.in/tutorials/image-convolution-examples/

## Slide 9: Detecting features: edge
We can use specific filters to identify features in an image
Consider: edges, corners, blobs, patterns (e.g., polka-dots, stripes)
Line detection with the combined filter
https://aishack.in/tutorials/image-convolution-examples/
Merge the 4 filters

## Slide 10: Detecting features: edge
We can use specific filters to identify features in an image
Consider: edges, corners, blobs, patterns (e.g., polka-dots, stripes)
Edge detection with the Sobel filter
https://aishack.in/tutorials/image-convolution-examples/
The Sobel filter
Notes: The previous operators are very prone to noise. The Sobel edge operators have a smoothing effect, so they're less affected to noise. Again, there's a horizontal component and a vertical component. It works by calculating the gradient of image intensity at each pixel within the image. It finds the direction of the largest increase from light to dark and the rate of change in that direction.

## Slide 11: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 12: Image Enhancement
Goal: improve the ‘visual quality’ of the image
  for human viewing
  for subsequent processing
Two typical methods
  spatial domain techniques....
    operate directly on image pixels
  frequency domain techniques....
    operate on the Fourier transform of the image
No general theory of ‘visual quality’
  General assumption: if it looks better, it is better
  Often not a good assumption

## Slide 13: Spatial Domain Methods
Transformation T
  point - pixel to pixel
  area - local area to pixel
  global - entire image to pixel
Neighborhoods
  typically rectangular
  typically an odd size: 3x3, 5x5, etc
  centered on pixel I(x,y)
Many IP algorithms rely on this basic notion
T(I(x,y))
I(x,y)
I’(x,y)
neighborhood N
I’(x,y) = T(I(x,y))
O=T(I)

## Slide 14: Noise Reduction
What is noise?
How is noise reduction performed?
  Noise reduction from first principles
  Neighbourhood operators
    linear filters (low pass, high pass)
    non-linear filters (median)
image
+
noise
=
‘grainy’ image

## Slide 15: Noise
Plot of image brightness.
Noise is additive.
Noise fluctuations are rapid
  high frequency.
Image
Noise
Image + Noise

## Slide 16: Noise
Noise varies above and below uncorrupted image.
Image
Image
+
Noise

## Slide 17: Noise Reduction - 1
How do we reduce noise?
Consider a uniform 1-d image and add noise.
Focus on a pixel neighbourhood.
Averaging the three values should result in a value closer to original uncorrupted data
Especially if gaussian mean is zero
Ai-1 Ai Ai+1
Ci

## Slide 18: Noise Reduction - 1
Averaging ‘smoothes’ the noise fluctuations.
Consider the next pixel Ai+1
Repeat for remainder of pixels.
Ai-1 Ai Ai+1 Ai+2
Ci+1

## Slide 19: Neighborhood Operations
All pixels can be averaged by convolving 1-d image A with mask B to give enhanced image C.
Weights of B must equal one when added together.
  Why?
C = A * B
B = [ B1 B2 B3 ]
Ci = Ai-1 ´B1 + Ai ´B2 + Ai+1 ´B3
B = [1 1 1]
Ci =
1
3
Ai-1 + Ai + Ai+1
3

## Slide 20: 2D Analog of 1D Convolution
Consider the problem of blurring a 2D image
Here’s the image and a blurred version:
How would we do this?
  What’s the 2D analog of 1D convolution?

## Slide 21: 2D Blurring Kernel
C = A * B
B becomes
1 1 1
1 1 1
1 1 1
B =
1
9

## Slide 22: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 23: Convolution
Extremely important concept in computer vision, image processing, signal processing, etc.
Lots of related mathematics (we won’t do)
General idea: reduce a filtering operation to the repeated application of a mask (or filter kernel) to the image
  Kernel can be thought of as an NxN image
  N is usually odd so kernel has a central pixel
In practice
  (flip kernel)
  Align kernel center pixel with an image pixel
  Pointwise multiply each kernel pixel value with corresponding image pixel value and add results
  Resulting sum is normalized by kernel weight
  Result is the value of the pixel centered on the kernel

## Slide 24: Example
Image
Kernel
Result
Image
Kernel is aligned with pixel in image, multiplicative sum is computed, normalized, and stored in result image.
Process is repeated across image.
What happens when kernel is near edge of input image?

## Slide 25: Convolution Size
Image size = M1 N1
Mask size = M2 N2
Convolution size =
M1- M2 +1 N1-N2+1
N1
N2
N1-N2+1
Typical Mask sizes
= 33, 5 5, 77,
9 9, 1111
What is the convolved
image size for a 128 
 128 image and
7  7 mask?

## Slide 26: Border Problem
missing samples are zero
missing samples are gray
copying last lines
reflected indexing (mirror)
circular indexing (periodic)
truncation of the result

## Slide 27: Convolution
= I M
*

## Slide 28: Noise Reduction - 1
Uncorrupted Image
Image + Noise
Image + Noise - Blurred

## Slide 29: Noise Reduction - 1
Technique relies on high frequency noise fluctuations being ‘blocked’ by filter. Hence, low-pass filter.
Fine detail in image may also be smoothed.
Balance between keeping image fine detail and reducing noise.

## Slide 30: Noise Reduction - 1
Saturn image coarse detail
Boat image contains fine detail
Noise reduced but fine detail also smoothed

## Slide 31: hmmmmm…..
Image
Blurred Image
-
=

## Slide 32: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 33: Noise Reduction - 2: Median Filter
Nonlinear Filter
Compute median of points in neighborhood
Has a tendency to blur detail less than averaging
Works very well for ‘shot’ or ‘salt and pepper’ noise
Original
Low-pass
Median
Notes: How does media filter work?
Get data from a window centered at the to-be-processed pixel
Sort the data (from min to max)
Put the median value in the filtered image

## Slide 34: Noise Reduction - 2
Low-pass
Median
Low-pass: fine detail smoothed by averaging
Median: fine detail passed by filter

## Slide 35: Summary
Summary
What is noise?
  Gaussian distribution
Noise reduction
  first principles
Neighbourhood
  low-pass
  median
Averaging pixels corrupted by noise cancels out the noise.
Low-pass can blur image.
Median may retain fine image detail that may be smoothed by averaging.
Conclusion

## Slide 36: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 37: Discontinuities
A: Depth discontinuity: abrupt depth change in the world
B: Surface normal discontinuity: change in surface orientation
C: Illumination discontinuity: shadows, lighting changes
D: Reflectance discontinuity: surface properties, markings
A
C
B
D

## Slide 38: Illusory Edges
Illusory edges will not be detectable by the algorithms that we will discuss
No change in image irradiance - no image processing algorithm can directly address these situations
Computer vision can deal with these sorts of things by drawing on information external to the image (perceptual grouping techniques)
Kanizsa Triangles

## Slide 39: Another One

## Slide 40: Goal
Devise computational algorithms for the extraction of significant edges from the image.
What is meant by significant is unclear.
  Partly defined by the context in which the edge detector is being applied

## Slide 41: Edgels
Define a local edge or edgel to be a rapid change in the image function over a small area
  implies that edgels should be detectable over a local neighborhood
Edgels are NOT contours, boundaries, or lines
  edgels may lend support to the existence of those structures
  these structures are typically constructed from edgels
Edgels have properties
  Orientation
  Magnitude
  Position

## Slide 42: Locating Edgels
Rapid change in image => high local gradient => differentiation
f(x) = step edge
1st Derivative f ’(x)
2nd Derivative -f ’’(x)
maximum
zero crossing

## Slide 43: Reality

## Slide 44: Properties of an Edge
Orientation
Original
Orientation
Magnitude
Position

## Slide 45: Quantitative Edge Descriptors
Edge Orientation
  Edge Normal - unit vector in the direction of maximum intensity change (maximum intensity gradient)
  Edge Direction - unit vector perpendicular to the edge normal
Edge Position or Center
  image position at which edge is located (usually saved as binary image)
Edge Strength / Magnitude
  related to local contrast or gradient - how rapid is the intensity variation across the edge along the edge normal.

## Slide 46: Edge Degradation in Noise
Ideal step edge
Step edge + noise
Increasing noise

## Slide 47: Edge Detection: Typical
Noise Smoothing
  Suppress as much noise as possible while retaining ‘true’ edges
  In the absence of other information, assume ‘white’ noise with a Gaussian distribution
Edge Enhancement
  Design a filter that responds to edges; filter output high are edge pixels and low elsewhere
Edge Localization
  Determine which edge pixels should be discarded as noise and which should be retained
    thin wide edges to 1-pixel width (nonmaximum suppression)
    establish minimum value to declare a local maximum from edge filter to be an edge (thresholding)

## Slide 48: Real Image

## Slide 49: Gradient Methods
F(x)
x
F’(x)
x
Edge= sharp variation
Large first derivative

## Slide 50: Gradient of a Function
Assume f is a continuous function in (x,y). Then
are the rates of change of the function f in the x and y directions, respectively.
The vector (Dx, Dy) is called the gradient of f.
This vector has a magnitude:
and an orientation:
q is the direction of the maximum change in f.
S is the size of that change.
Dx
Dy
q = tan-1 ( )

## Slide 51: Geometric Interpretation
But
  I(i,j) is not a continuous function.
Therefore
  look for discrete approximations to the gradient.

## Slide 52: Discrete Approximations
df(x)
dx
= lim
Dx 0
f(x + Dx) - f(x)
Dx
df(x)
dx
f(x) - f(x-1)
1
@
x
x-1
f(x)
Convolve with -1 1

## Slide 53: In Two Dimensions
Discrete image function I
Derivatives Differences
-1 1
1
-1
DjI =
DiI =

## Slide 54: 1x2 Example
1x2 Vertical
1x2 Horizontal
Combined

## Slide 55: Smoothing and Edge Detection
Derivatives are 'noisy' operations
  edges are a high spatial frequency phenomenon
  edge detectors are sensitive to and accent noise
Averaging reduces noise
  spatial averages can be computed using masks
Combine smoothing with edge detection.

## Slide 56: Effect of Blurring
Original
Orig+1 Iter
Orig+2 Iter
Image
Edges
Thresholded
Edges

## Slide 57: Combining the Two
Applying this mask is equivalent to taking the difference of averages on either side of the central pixel.

## Slide 58: Many Different Kernels
Variables
  Size of kernel
  Pattern of weights
1x2 Operator (we’ve already seen this one
-1 1
1
-1
DjI =
DiI =

## Slide 59: Roberts Cross Operator
Does not return any information about the orientation of the edge
or
1 0
0 -1
0 1
-1 0
+
| I(x, y) - I(x+1, y+1) | + | I(x, y+1) - I(x+1, y) |
[ I(x, y) - I(x+1, y+1) ]2 + [ I(x, y+1) - I(x+1, y) ]2
S =
S =

## Slide 60: Sobel Operator
-1 -2 -1
0 0 0
1 2 1
-1 0 1
-2 0 2
-1 0 1
S1=
S2 =
Edge Magnitude =
Edge Direction =
S1 + S2
2
2
tan-1
S1
S2
Notes: S1, S2 represent response to the kernels. Not the kernel themselves

## Slide 61: Anatomy of the Sobel
Sobel kernel is separable!
Averaging done parallel to edge
1/4
1/4
+
Notes: Explain how this is done.

## Slide 62: Prewitt Operator
-1 -1 -1
0 0 0
1 1 1
-1 0 1
-1 0 1
-1 0 1
P1=
P2 =
Edge Magnitude =
Edge Direction =
P1 + P2
2
2
tan-1
P1
P2
Notes: P1, P2 represent response, not the kernels

## Slide 63: Analysis of Edge Kernels
Analysis based on a step edge inclined at an angle q (relative to y-axis) through center of window.
Robinson/Sobel: true edge contrast less than 1.6% different from that computed by the operator.
Error in edge direction
  Robinson/Sobel: less than 1.5 degrees error
  Prewitt: less than 7.5 degrees error
Summary
  Typically, 3 x 3 gradient operators perform better than 2 x 2.
  Prewitt2 and Sobel perform better than any of the other 3x3 gradient estimation operators.
  In low signal to noise ratio situations, gradient estimation operators of size larger than 3 x 3 have improved performance.
  In large masks, weighting by distance from the central pixel is beneficial.

## Slide 64: Prewitt Example
Santa Fe Mission
Prewitt Horizontal and Vertical Edges Combined

## Slide 65: Edge Thresholding
Global approach
See Haralick paper for thresholding based on statistical significance tests.
64
128
T=64
T=128
Edge Histogram

## Slide 66
Second derivatives…

## Slide 67: Edges from Second Derivatives
Digital gradient operators estimate the first derivative of the image function in two or more directions.
f(x) = step edge
1st Derivative f’(x)
2nd Derivative -f’’(x)
maximum
zero crossing
GRADIENT
METHODS

## Slide 68: Second Derivatives
Second derivative = rate of change of first derivative.
Maxima of first derivative = zero crossings of second derivative.
For a discrete function, derivatives can be approximated by differencing.
Consider the one-dimensional case:
D f(i) = D f(i+1) - D f(i)
2
= f(i+1) - 2 f(i) + f(i-1)
Mask:

## Slide 69: Laplacian Operator
Now consider a two-dimensional function f(x,y).
The second partials of f(x,y) are not isotropic.
Can be shown that the smallest possible isotropic second derivative operator is the Laplacian:
Two-dimensional discrete approximation is:

## Slide 70: Example Laplacian Kernels
Note that these are not the optimal approximations to the Laplacian of the sizes shown.
5X5
9X9

## Slide 71: Example Application
5x5 Laplacian Filter
9x9 Laplacian Filter

## Slide 72: Detailed View of Results

## Slide 73: Laplacian Enhancement
Blurred Original
3x3 Laplacian Enhanced

## Slide 74: Noise
Second derivative, like first derivative, enhances noise
Combine second derivative operator with a smoothing operator.
Questions:
  Nature of optimal smoothing filter.
  How to detect intensity changes at a given scale.
  How to combine information across multiple scales.
Smoothing operator should be
  'tunable' in what it leaves behind
  smooth and localized in image space.
One operator which satisfies these two constraints is the Gaussian:

## Slide 75: 2D Gaussian Distribution
The two-dimensional Gaussian distribution is defined by:
From this distribution, can generate smoothing masks whose width depends upon s:

## Slide 76: s Defines Kernel ‘Width’
s2 = .25
s2 = 1.0
s2 = 4.0

## Slide 77: Creating Gaussian Kernels
The mask weights are evaluated from the Gaussian distribution:
This can be rewritten as:
This can now be evaluated over a window of size nxn to obtain a kernel in which the (0,0) value is 1.
k is a scaling constant
W(i,j) = k * exp (- )
i2 + j2
2 s2
= exp (- )
i2 + j2
2 s2
W(i,j)
k

## Slide 78: Example
Choose s = 2. and n = 7, then:
2
-3
-2
-1
0
1
2
3
-3
-2
-1
0
1
2
3
i
j

## Slide 79: Example
7x7 Gaussian Filter
Plot of Weight Values

## Slide 80: Kernel Application
7x7 Gaussian Kernel
15x15 Gaussian Kernel

## Slide 81: Why Gaussian for Smoothing
Gaussian is not the only choice, but it has a number of important properties
  If we convolve a Gaussian with another Gaussian, the result is a Gaussian
    This is called linear scale space
  Efficiency: separable
  Central limit theorem

## Slide 82: Why Gaussian for Smoothing
Gaussian is separable

## Slide 83: Why Gaussian for Smoothing – cont.
Gaussian is the solution to the diffusion equation
We can extend it to non-linear smoothing

## Slide 84: Ñ2G Filter
Marr and Hildreth approach:
  1. Apply Gaussian smoothing using s's of increasing size:
  2. Take the Laplacian of the resulting images:
  3. Look for zero crossings.
Second expression can be written as:
Thus, can take Laplacian of the Gaussian and use that as the operator.

## Slide 85: Mexican Hat Filter
Laplacian of the Gaussian
Ñ2G is a circularly symmetric operator.
Also called the hat or Mexican-hat operator.

## Slide 86: s2 Controls Size
s2 = 0.5
s2 = 1.0
s2 = 2.0

## Slide 87: Kernels
Remember the center surround cells in the human system?
5x5
17 x 17

## Slide 88: Example
13x13 Kernel

## Slide 89: Example
13 x 13 LoG Filter
Thesholded Positive
Thesholded Negative
Zero Crossings

## Slide 90: Scale Space
Thresholded Negative
17x17 LoG Filter
Thresholded Positive
Zero Crossings

## Slide 91: Scale Space
s2 = 2
s2 = 2
s2 =2 2
s2 = 4

## Slide 92: Multi-Resolution Scale Space
Observations:
  For sufficiently different s 's, the zero crossings will be unrelated unless there is 'something going on' in the image.
  If there are coincident zero crossings in two or more successive zero crossing images, then there is sufficient evidence for an edge in the image.
  If the coincident zero crossings disappear as s becomes larger, then either:
    two or more local intensity changes are being averaged together, or
    two independent phenomena are operating to produce intensity changes in the same region of the image but at different scales.
Use these ideas to produce a 'first-pass' approach to edge detection using multi-resolution zero crossing data.

## Slide 93: Color Edge Detection
Typical Approaches
  Fusion of results on R, G, B separately
  Multi-dimensional gradient methods
  Vector methods
  Color signatures: Stanford (Rubner and Thomasi)

## Slide 94: Outline
Convolution: an Introduction
Image Enhancement: Noise Reduction (1)
Convolution: a Revisit
Image Enhancement: Noise Reduction (2)
Edge Detection
An Example: SIFT

## Slide 95: SIFT features
Scale-invariant feature transform (SIFT): detects local features in an image [Lowe, 1999].
These local features are called keypoints.
The SIFT features for the keyponts are invariant to scale, illumination, and rotation.
Each keypoint is represented with a 128-dimensional SIFT vector
Notes: SIFT is used to detect local features in an image. They are called keypoints in the image.
In step 2, , for a given keypoint, warp the region around it to canonical orientation and scale and resize the region. So images with different rotations are transformed to the same orientation for the same keypoint.
Why is SIFT invariant to scale?
This means that it finds the scale of the image which the feature will produce the highest response. Then, the descriptor is calculated in that scale. So when you use a smaller/larger version, it should still find the same scale for the feature.
Why is SIFT invariant to illumination/brightness?
A brightness change in which a constant is added to each image pixel will not affect the gradient values, as they are computed from pixel differences. Therefore, the descriptor is invariant to affine changes in illumination.
To get rotation invariance, Lowe proposed to find the main orientation of the descriptor, and assign that angle to the keypoint. Using this information, it becomes easy to compare two keypoints.

## Slide 96: SIFT features
First, detect keypoints using the SIFT detector, which also detects scale and orientation of the keypoint.
Next, for a given keypoint, warp the region around it to canonical orientation and scale and resize the region to 16X16 pixels.
https://gilscvblog.com/2013/08/18/a-short-introduction-to-descriptors/

## Slide 97: SIFT features
Compute the gradient for each pixel (orientation and magnitude).
Divide the pixels into 16, 4X4 pixels squares.
https://gilscvblog.com/2013/08/18/a-short-introduction-to-descriptors/
Notes: An image gradient is defined as a directional change in image intensity. Different kernels such as Sobel, Prewitt, etc are derived to use convolution to approximate the gradient. The gradient orientation points in the direction of the largest possible intensity increase. The magnitude is the rate of change in that direction.
X-gradient will find vertical edges and y-gradient will find horizontal edges because edges in an image have abrupt change in the intensity values. Therefore, the largest values will occur across an edge. Edges are perpendicular to the gradient direction(largest). That is why we can use gradients for edge detection.

## Slide 98: SIFT features
For each square, compute gradient direction histogram over 8 directions
6. Concatenate the histograms to obtain a 128 (16*8) dimensional feature vector:
https://gilscvblog.com/2013/08/18/a-short-introduction-to-descriptors/

## Slide 99: SIFT features:
SIFT features can be used to
  align images
  rotate, scale, reshape images
  characterize and compare images:
  bag-of-SIFT-features
  Each keypoint has a 128-d SIFT feature vector

## Slide 100: Summary
Convolution: an Introduction
Image Enhancement: Noise Reduction (1) - lowpass
Convolution: a Revisit
Image Enhancement: Noise Reduction (2) - median
Edge Detection – first and second order detectors
An Example: SIFT